Eflare Beacons Testing and Accreditation Information

Below is a summary of the completed tests and accreditations for the Eflare Transit Eflare Flagging Lantern and Transit Eflare Magnetic Base;

Transit Specification for Light Emitting Diode (LED) Flagging Lantern - Section 82A.

| Test Requirement | Section 82A | Eflare Test Report Number | Tested By |
| --- | --- | --- | --- |
| Dimensions | Para 82.2.4 | TR161003_07 | Steve Jenkins & Associates Pty Ltd |
| Chromaticity | Para 82.2.1.D.2 | TR161003_02AFR TR161003_02GFR TR161003_02RFR | Steve Jenkins & Associates Pty Ltd |
| Flash Rate | Para 82.2.1.D.3 | TR161003_02AFR TR161003_02GFR TR161003_02RFR | Steve Jenkins & Associates Pty Ltd |
| Minimum Candelas | Para 82.2.1.D.4 Using – para 82.5.4 | TR161003_02AFR TR161003_02GFR TR161003_02RFR | Steve Jenkins & Associates Pty Ltd |
| Average Light Output | Para 82.2.1.D.5 Using – para 82.5.4 | TR161003_02AFR TR161003_02GFR TR161003_02RFR | Steve Jenkins & Associates Pty Ltd |
| Rain Test | Para 82.5.1 | CT2153-1 | QPS Evaluation Services Inc. |
| Aged Gasket Test | Para 82.5.1 | 180470 | VicLab Pty Ltd |
| Drop Test | Para 82.2.3 | TR161003_04 | Steve Jenkins & Associates Pty Ltd |
| Performance | Para 82.2.3 | TR161003_05R | Steve Jenkins & Associates Pty Ltd |
| Work Shift Endurance | Para 82.5.5 A&B | TR161003_05R | Steve Jenkins & Associates Pty Ltd |
| Low Battery Indicator | Para 82.5.5 C&D | TR161003_06 | Steve Jenkins & Associates Pty Ltd |
| Stability Test | Para 82.5.3 | TR161003_03R | Steve Jenkins & Associates Pty Ltd |
| Magnetic Strength Test | Para 82.5.6 A&B | Ref SO 266273 | Integrated Magnetics |

Additional Accreditation for the Eflare beacons;

The Eflare Beacons are compliant with the publications IEC 60079 Part 0 (General requirements) and Part 11 (Intrinsic Safety “i”) and as listed below;

IEC60079-0: 2004 Edition 4

IEC60079.11: 2006 Edition 5

IEC60529: 2001 Edition 2.1

Eflare new accreditation;

Accreditation Level - Ex ic IIC T4 Gc IP66

ATEX Certificate No. – ITS10ATEX27129

IECEx Certificate No. – IECEx TSA 11.0023

Social Compliance

The manufacturing facility for the Eflare beacons has been independently verified as being to a SA8000 standard for Social Compliance.

Certificate number: 17 114 1732804

Auditor: TÜV Rheinland